Cisco IOS commands

Privileged Mode

enable - get to privileged mode
disable - get to user mode
enable password - sets privileged mode password
enable secret - sets encrypted privileged mode password

Setting Passwords

enable secret - set encrypted password for privilegedaccess
enable password - set password for privileged access (used when there is no enable secret and when using older software)
Set password for console access:
(config)#line console 0
(config-line)#login 
(config-line)#password 
Set password for virtual terminal (telnet) access (password must be set to access router through telnet):
(config)#line vty 0 4 
(config-line)#login 
(config-line)#password 
Set password for auxiliary (modem) access:
(config)#line aux 0
(config-line)#login 
(config-line)#password

Configuring the Router

sh running-config - details the running configuration file (RAM)
sh startup-config - displays the configuration stored in NVRAM
setup - Will start the the automatic setup; the same as when you first boot the router
config t - use to execute configuration commands from the terminal
config mem - executes configuration commands stored in NVRAM; copies startup-config to running-config
config net - used to retrieve configuration info from a TFTP server
copy running-config startup-config - copies saved config in running config (RAM) to NVRAM or "write memory" for IOS under ver.11
copy startup-config running-config - copies from non-volatile (NVRAM) to current running config (RAM)
boot system flash - tells router which IOS file in flash to boot from
boot system tftp - tells router which IOS file on the tftp server to boot from
boot system rom - tell router to boot from ROM at next boot
copy flash tftp - Copies flash to tftp server
copy tftp flash - Restores flash from tftp server
copy run tftp - Copies the current running-config to tftp server
copy tftp run - Restores the running-config from tftp server

General Commands

no shutdown - (enables the interface)
reload - restarts the router
sh ver - Cisco IOS version, uptime of router, how the router started, where system was loaded from, the interfaces the POST found, and the configuration register
sh clock - shows date and time on router
sh history - shows the history of your commands
sh debug - shows all debugging that is currently enabled
no debug all - turns off all debugging
sh users - shows users connected to router
sh protocols - shows which protocols are configured
banner motd # Your_message # - Set/change banner
hostname - use to configure the hostname of the router
clear counters - clear interface counters

Processes & Statistics

sh processes - shows active processes running on router
sh process cpu - shows cpu statistics
sh mem - shows memory statistics
sh flash - describes the flash memory and displays the size of files and the amount of free flash memory
sh buffers - displays statistics for router buffer pools; shows the size of the Small, Middle, Big, Very Big, Large and Huge Buffers
sh stacks - shows reason for last reboot, monitors the stack use of processes and interrupts routines

CDP Commands (Cisco Discovery Protocol uses layer 2 multicast over a SNAP-capable link to send data):

sh cdp neighbor - shows directly connected neighbors
sh cdp int - shows which interfaces are running CDP
sh cdp int eth 0/0 - show CDP info for specific interface
sh cdp entry - shows CDP neighbor detail
cdp timer 120 - change how often CDP info is sent (default cdp timer is 60)
cp holdtime 240 - how long to wait before removing a CDP neighbor (default CDP holdtime is 180)
sh cdp run - shows if CDP turned on
no cdp run - turns off CDP for entire router (global config)
no cdp enable - turns off CDP on specific interface

Miscellaneous Commands

sh controller t1 - shows status of T1 lines
sh controller serial 1 - use to determine if DCE or DTE device
(config-if)#clock rate 6400 - set clock on DCE (bits per second)
(config-if)#bandwidth 64 - set bandwidth (kilobits)

IP Commands
Configure IP on an interface:

int serial 0
ip address 157.89.1.3 255.255.0.0
int eth 0 
ip address 2008.1.1.4 255.255.255.0

Other IP Commands:

sh ip route - view ip routing table
ip route [administrative_distance] - configure a static IP route
ip route 0.0.0.0 0.0.0.0 - sets default gateway
ip classless - use with static routing to allow packets destined for unrecognized subnets to use the best possible route
sh arp - view arp cache; shows MAC address of connected routers
ip address 2.2.2.2 255.255.255.0 secondary - configure a 2nd ip address on an interface
sh ip protocol

IPX Commands
Enable IPX on router:

ipx routing
Configure IPX + IPX-RIP on an int:
int ser 0
ipx network 4A

Other Commands:

sh ipx route - shows IPX routing table
sh ipx int e0 - shows ipx address on int
sh ipx servers - shows SAP table
sh ipx traffic - view traffic statistics
debug ipx routing activity - debugs IPS RIP packets
debug ipx sap - debugs SAP packets

Routing Protocols
Configure RIP:

router rip
network 157.89.0.0
network 208.1.1.0
Other RIP Commands:
debug ip rip - view RIP debugging info
Configure IGRP:
router IGRP 200
network 157.89.0.0
network 208.1.1.0

Other IGRP Commands:
debug ip igrp events - view IGRP debugging info
debug ip igrp transactions - view IGRP debugging info

Access Lists (see notes below for details)

sh ip int ser 0 - use to view which IP access lists are applies to which int
sh ipx int ser 0 - use to view which IPX access lists are applies to which int
sh appletalk int ser 0 - use to view which AppleTalk access lists are applies to which int

View access lists:

sh access-lists
sh ip access-lists
sh ipx access-lists
sh appletalk access-lists

Apply standard IP access list to int eth 0:

access-list 1 deny 200.1.1.0 0.0.0.255
access-list 1 permit any
int eth 0
ip access-group 1 in
Apply Extended IP access list to int eth 0:
access-list 100 deny tcp host 1.1.1.1 host 2.2.2.2 eq 23
access-list 100 deny tcp 3.3.3.0 0.0.0.255 any eq 80
int eth 0
ip access-group 100 out
Apply Standard IPX access list to int eth 0:
access-list 800 deny 7a 8000
access-list 800 permit -1
int eth 0
ipx access-group 800 out
Apply Standard IPX access list to int eth 0:
access-list 900 deny sap any 3378 -1
access-list 900 permit sap any all -1
int eth 0
ipx access-group 900 out

Wan Configurations (see notes below for more details)

PPP Configuration
encapsulation ppp
ppp authentication 
ppp chap hostname 
ppp pap sent-username 
sh int ser 0 - use to view encapsulation on the interface

Frame-Relay Configuration

encapsulation frame-relay ietf - use IETF when setting up a frame-relay network between a Cisco router and a non-Cisco router
frame-relay lmi-type ansi - LMI types are Cisco, ANSI, Q933A; Cisco is the default; LMI type is auto-sensed in IOS v11.2 and up
frame-relay map ip 3.3.3.3 100 broadcast - if inverse ARP won't work, map Other IP to Your DLCI # (local)
keepalive 10 - use to set keepalive
sh int ser 0 - use to show DLCI, LMI, and encapsulation info
sh frame-relay pvc - shows the configured DLCI's; shows PVC traffic stats
sh frame-relay map - shows route maps
sh frame-relay lmi - shows LMI info

Keyboard Shortcuts

CTRL-P - show previous command
CTRL-N - show next command
SHIFT-CTRL-6 - Break