Intro to Network Security Firewalls

Objectives:

You should be able to:

- Describe each of the following: border router, static and dynamic NAT, and PAT, and also define what they can and cannot accomplish security-wise.

- Describe the different types of firewalls: Circuit, Proxy, Guard, Packet, Stateful, Personal including how they differ in an example attack that each can fend off.

- Describe 3 firewall vulnerabilities

- Draw a couple of secure configurations for a large corporation and describe the advantages of each configuration.

- Describe what a firewall policy is, give an example policy, and indicate how a policy may be used

- Describe how firewalls are audited

## Alternatives to (or Optional Features within) Firewalls

Screening or Border Router:

Screens incoming packets IP addresses

- Disadvantage: Only screens incoming packet IP addresses

- Can be combined with a Circuit or Proxy Firewall for additional safety

Often router and firewall work together = layered defense.  Some mirror rules for critical services.

### Network Address Translation (NAT)

- Reduces number of IP addresses necessary by keeping pool of globally routable IP addresses

- Translates an external IP address into internal IP addresses

Static NAT: One external IP address translates into one fixed internal IP address

Dynamic NAT: Internal IP addresses are assigned an external IP address on a First Come First Serve basis.

Port Address Translation (PAT) or Hide NAT:

- Translates one incoming IP address/port into an internal IP address/port.  Multiple internal IP addresses can map to one external IP address

- IPsec has difficulties

Security advantage:

- Connections must initiate from inside.  No way of translating IP address if no table entry exists.

- But does not:

- Track current sequence numbers

- Verify content is safe

## Firewalls

Firewall:

A network device that implements access control for a network

Required Functions:

- Serve as an entry point into a network

- Screens all packets entering the network

- Log and alarm events

- Perform Network Address Translation functions (optional)

- Perform Virtual Private Network functions (optional)

- Support no other functions (that can be compromised)

### Types of Firewalls

Packet Filters: Examines IP (and sometimes TCP/UDP) headers and filters packets based on rules

- Generally filter on Source/Destination IP address, TCP/UDP port numbers. High throughput, low delay

- Can perform Ingress & Egress filtering

- Problem:  In heavy load may forward all packets without logging

- Problem:  Cannot catch application-level errors

- ICMP can have invalid contents

- FTP, RPC use ports > 1023, dynamically allocated

- Cannot recognized spoofed IP or port addresses

- Routers can do packet filtering, most firewalls do more

IP  Header                               TCP Header             Application Header & Data

| … | Prot | Src Addr | Dest Addr | … | … | Src Port | Dest Port |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

IP  Header                               TCP Header                      Application Header & Data

| … | Prot | Src Addr | Dest Addr | … | … | Src Port | Dest Port | Flags | Seq No |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Stateful Packet Filters

Tracks TCP/UDP connection status

- Can configure outbound-only connections

- Packets are allowed in if connection is established

- Records source/destination IP and port addresses, protocol (TCP/UDP), timer expiration

- TCP: Also supports TCP state, Sequence numbers

- UDP: Supports expiration timer, pseudo state

- May prevent fragmentation attacks

- Advantage:  Supports higher loads than Circuit-Level Firewalls at same memory/processor speed levels

- Problems

- ICMP: Messages may come from intermediate node, not destination.  Must accept/reject all ICMP messages of type N

- DOS Attack: Establish connections to fill table

- Applications change ports or use multiple ports

- Application attacks not detected since application protocols not scanned

- Some routers support Stateful packet filtering; nearly all firewalls do.

- Firewalls include: CISCO PIX; Checkpoint Firewall-1, Linux Netfilter, Netscreen, etc.

Stateful Inspection Filters:

- Can perform access-control functions for applications: HTTP, etc.

- Can decode ICMP messages

- Can control FTP active/passive sessions

- Can support multiple connections of RealAudio, MS Distributed Component Object Model (DCOM)

- In some cases minimal application filtering may be supported

Circuit-Level Firewalls or Proxy Server:

Establishes a TCP connection with remote end before passing information through.

- Creates two sessions: one with sender & one with receiver

- Does not filter based on packet contents (other than state)

- Also known as Pass-Through Proxy or Generic Proxy

- Advantages: If firewall failure, no packets are forwarded through firewall

- Catches fragmentation errors

- Problems:

- Does not detect invalid data

- Moves security issues from service to firewall: e.g., DOS attacks

- Less able to handle high loads since each connection becomes two

- Requires much greater memory and processor at application level (Web page is > 1 connection)

- Slower interfaces can result in poor performance for streaming applications

IP  Header                                   TCP Header                     Application Header & Data

| … | Prot | Src Addr | Dest Addr | Frag | … | … | Src Port | Dest Port | Flags | Seq No |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Application Proxy Firewall:

Examines packets and their contents at the Application Layer

- Can cause delay due to additional processing

- May strip info on internal servers, server version on outgoing messages (e.g., email)

- May allow only certain types of sessions through:

FTP: May permit receives, no sends.  Or sends of specific files only.

Email:  Encrypts email between all of company’s offices

HTTP: May filter PUT commands, URL names.  Can cache replies.

Authentication:  Perform extra authentication for external access (via dialup or internet)

IP  Header                                   TCP Header                    Appl. Hdr       App Data

| … | Prot | Src Addr | Dest Addr | Frag | … | … | Src Port | Dest Port | Flags | Seq No | Appl Hdr |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Guard Firewall:

A sophisticated application proxy firewall.  For example:

- Filters email and file transfers through virus scanner

- Limits email transmission per user to threshold value

IP  Header                                   TCP Header                    Appl. Hdr       App Data

| … | Prot | Src Addr | Dest Addr | Frag | … | … | Src Port | Dest Port | Flags | Seq No | Appl Hdr | Application Data |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Example Proxy Firewalls:

- Network Associate’s Gauntlet, Symantec Enterprise, BorderWare, WinGate, T.REX Open Source, Squid

- Squid: Supports HTTP, FTP, Gopher

- For HTTP: Filters IP addresses, URL substrings (e.g. ‘port’), user level authentication, GET or POST commands, filters inbound banner adds, caches http replies

Personal Firewalls: Protects a personal computer

- Allows access only to single computer

- Protects against attacks from within the network

- May or may not filter at application layer

- Requires policy definition for downloading code, data sharing, permissible access

- Often combined with virus scanner

Positioning & Maintenance of Firewall

- Zoning:  Clear separation of private vs. public vs. DMZ

- Entry Point: Only one way in – through the firewall (Minimize # entries)

- Stateful Support: Requires same entry/exit route into network

- Layered Firewall: Firewall deployed in series

- Can provide dual security & redundancy

- Maximize logging at perimeter

- Maintain firewall & review logs to recognize deviations from norm

- Monitor traffic before closing (or disabling) ports

### Configurations:

Border Router & Firewall: Layered Defense

- Router makes network resistant to DOS

- Use mirror rules for critical services

For Larger Companies:

- Dual Firewalls: Side-by-Side

- Packets directed to firewall that handles specific applications (e.g., VPN firewall)

- Border Router reduces DOS attacks

- Dual Inline (or cascading) Firewalls provide redundancy

Dual Inline Firewalls

- Border Router reduces DOS attacks

- Uses different brands of firewalls to protect against firewall software errors

- Processor-intensive

- First Firewall can do VPN decryptions, Second firewall can do security checks.

What about the following diagram?

### Firewall Vulnerabilities

- Firewalls can be bypassed via other means (e.g., modem, CDs)

- Data transmitted to the outside may be vulnerable

- Firewalls may lie: in heavy loads attack packets may get through without logging.

- Extra software on the firewall device increase vulnerability

Firewalls are vulnerable if installed above a general-purpose OS

- Firewalls do not prevent malicious acts within the network

- Layers of defense are safer than a single firewall

- Auditing:  Scan weekly or at every change

- Retain a baseline of perimeter device configurations

#### An Example: CISCO PIX Firewall:

Rules:

- No packets can traverse the firewall without a translation, connection and state.

- Outbound connections are allowed, except when expressly forbidden

- Inbound connections are denied, except when expressly allowed

- All ICMP packets are denied, except when expressly allowed

- All attempts to circumvent the previous rules are denied and logged

Zoning:

- 10 interfaces

- 100 security levels:

0 is low, 100 is most secure

Low(High security: Rules must be explicitly defined

High(Low security:  Traffic can move freely

Features

Stateful TCP/UDP filtering  tracks:

- TCP sequence numbers and additional TCP flags

Validates packets for the current state

Uses safer more-random sequence numbers

Forwards connection request only after 3-way handshake is complete

UDP packet flow & timers

Transmission out sets a timer; transmissions in must occur within a given time period

Monitors configurable timers

Non-Stateful Routing/IP/TCP Protocol Processing:

- Basic routing using Routing Information Protocol (RIP)

- NAT and PAT translation

- Alias:  Translation of internal illegal addresses to legal addresses

- Access Control Lists can define which IP addresses, protocol numbers, and/or port numbers shall be allowed

- Unicast Reverse Path Forwarding: Prevents source IP address spoofing

- Virtual (Fragmentation) Reassembly: Filters IP/TCP headers regardless of fragmentation

Application-Level Filtering:

- Proxy Authentication: For connection requests from outside, for HTTP, Telnet or FTP session, via TACACS+, Radius, or Cisco Secure Authentication techniques

Flood Guard:  Limits number of invalid attempts

- DNS Guard: Drops multiple DNS responses to thwart DNS flooding attacks

- Websense: Filters outgoing URL requests at Websense server

- Mail Guard:  Allows seven email commands only: HELO, MAIL, RCPT, DATA, RSET, NOOP, QUIT

- Fixup Protocol: When services require two TCP port numbers, listens for second port number to allow it:  FTP, HTTP, SMTP, RSH, SQLNET, H.323

- Multimedia: Interprets IP and port addresses buried in multimedia applications (e.g. H.323 VoIP)

- VPN: Using DES or 3DES encryption

- Integrated with Cisco IDS

Operational Features:

- Selective logging on connection failures, errors, authentication events, failover, application (FTP or URL) events, SNMP (mail) events, routing errors, PIX management events

- Failover with standby system

- Cisco Secure Policy Manager: Cisco network management if entire network is Cisco.

- No OS vulnerabilities, No software installation

### Configuring and Auditing Firewalls(/Routers)

Designing Firewalls/Routers

- Before creating a firewall configuration, create firewall policies.

Firewall policy: An Access Control List (ACL) item in English

- Policies can be reviewed, turned into ACLs, and tested

- Example Policy:  IP addresses with internal source addresses shall not be allowed into the internal network from the outside.

- Often ports > 1000 cannot be closed due to applications like FTP

- Other policies may deal with failover protection, detecting malicious code, …

Configuring Firewalls/Routers

- Put specific rules first, then general rules

- When a rule matches, no further testing is done.

- Minimize tests & speed processing by placing common rules first

Auditing Firewalls:

- If there is no security policy, speak with mgmt about their expectations of the firewall

- After configuring the firewall, test the firewall by launching an attack

- Use a sniffer to determine which attack packets get through

- Other required operations include:

Log Monitoring and Notification

User Mgmt and Password policy

Patch Update and Backup

Change Control

Secure build for firewall platforms

Audit Testing

- Scan all TCP and UDP ports 0-65,535 on the firewall

- Ping devices to see if Echo Requests pass

- Scan using ‘TCP Connect Scan’ (Full SYN-ACK)

- Do a slow SYN scan (with 15 second delay) to se if port scans are detected (by IDS)

- Scan with FINs, ACKs, and fragmented ACKs , Xmas Tree scans (URG, PUSH, FIN flags) to see how all perform

- Scan the subnet using UDP ports to look for open applications

- Check routing capability, including NAT

- Test other blocked source IP addresses: Spoofed, private, loopback, undefined

- Test other protocols: ICMP, IP fragmentation, all policies, all directions.

- Verify logging occurs for illegal probes

Always get signed-off permission first!!!

Audit Test Tools:

- Sniffers: Ethereal, tcpdum, windump

- Network Mapping Tools: Nmap, hping, nemesis (packet generation tool)

- Active Vulnerability Testing: Nessus

# Text boxes

N
A
T

x

Dynamic NAT:  Single external IP address may translate into many IP addresses.

N
A
T

x

y

Hide NAT or PAT: IP/Port translates to IP/Port

x

N
A
T

Static NAT:  External IP address translates into Internal IP address.

Bit

Bucket

Firewall