- Obtain VIPs if they do not exist

- Update the cluster object topology to reflect correct VIPs.

- Create host object for "Multicast-VRRP" on IP 224.0.0.18

- Create rule with SRC=<firewall objects>, DST=Multicast-VRRP, SVC=ospf.  Logging is off!

- 3rd Party config: mode=HA, Nokia VRRP, check State Sync, Check "Forward Cluster...".

- Push policy.

- Add static routes (if necessary) to 170.186.139.128/25 and 167.16.7.0/24.

- VRRP config, monitored circuit:

- Primary=254, secondary 245, delta 11 on monitored interfaces

- monitor firewall on primary, not on secondary.

- preempt mode disabled on primary, enabled on secondary

- Accept connections to VRRP IPs enabled on both.

- hello interval 1.

- Verify VRRP status on both.

- Enable virtual address in OSPF on secondary.

- Enable virtual address in OSPF on primary.

- Validate traffic.  Should have no dropped sessions.