How to upgrade Juniper IOS from 5.4.x to 6.x

Juniper requires you to upgrade the boot loader prior to upgrading your IOS from 5.4 to 6.x.

The boot loader file for 6.0 is:

The procedure is explained below:

Upgrade sequence—Juniper Networks recommends that you follow the upgrade instructions described in the ScreenOS Upgrade Guide located at

http://www.juniper.net/techpubs/software/screenos/screenos6.0.0/upgrade_guide.pdf.

If you upgrade directly from ScreenOS 5.0.0 or ScreenOS 5.1.0 to ScreenOS 6.0, you risk losing part of any existing configuration. For ISG 2000 devices, you must upgrade to an intermediate firmware and upgrade the boot loader before upgrading to the ScreenOS 6.0 firmware. Refer to Upgrade Paths to ScreenOS 6.0 in the ScreenOS Upgrade Guide for intermediate software and boot loader upgrade information.

Refer to the following procedure to upgrade the SSG 500/SSG500M boot loader:

1. Download the boot loader image (v.1.0.3) from the Juniper Networks support site to the root directory of your TFTP server. (the TFTP server must be on the same subnet as your firewall).

2. Log into http://www.juniper.net/customers/support/.

3. In the Download Software section, click ScreenOS Software.

4. Download the latest SSG 500/SSG 500M boot loader and save it to the root directory of your TFTP server (the TFTP server must be on the same subnet as your firewall).

5. If necessary, start the TFTP server.

6. Make an Ethernet connection from the device hosting the TFTP server to the MGT port on the SSG 500 and a serial connection from your workstation to the console port on the SSG 500.

7. Restart the SSG 500 by entering the reset command. When prompted to confirm the command--System reset, are you sure? y/[n]--press the Y key.

The following system output appears:

NetScreen SSG500 BootROM V1.0.2 (Checksum: 8796E2F3)

Copyright (c) 1997-2004 NetScreen Technologies, Inc.

Total physical memory: 512MB

Test - Pass

Initialization................ Done

1. Press the X and A keys sequentially to update the boot loader.

2. Enter the filename for the boot loader software you want to load (for example, Boot2.1.0.3), the IP address of the SSG 500, and the IP address of your TFTP server. The following system output appears:

File Name [boot2.1.0.2]: boot2.1.0.3

Self IP Address [xxx.xxx.xxx.xxx]:

TFTP IP Address [xxx.xxx.xxx.xxx]:

1. Press the Enter key to load the file. The following system output appears:

Save loader config (112 bytes)... Done

Loading file "boot2.1.0.3"...

/

Loaded successfully! (size = 125,512 bytes)

Ignore image authentication!

...

.......................

Complete:

You can now proceed to the normal IOS upgrade procedure (via NSM and/or GUI)